<!DOCTYPE HTML PUBLIC "-//IETF//DTD HTML//EN">

Boeing 747-400

|  | COCKPIT SAFETY CHECK |  |
| --- | --- | --- |
| Battery Switch |  | . . . . . . . . . . . . . . . . . . . . . . . . . .ON |
| Standby Power Switch |  | . . . . . . . . . . . . . . . . AUTO |
| Hydraulic Demand Pumps |  | . . . . . . . . . . . . . . OFF |
| Windshield Wiper Switches |  | . . . . . . . . . . . . . .OFF |
| Alternate Flap Selector |  | . . . . . . . . . . . . . . . . . .OFF |
| Landing Gear Lever |  | . . . . . . . . . . . . . . . . . . . . DOWN |
| Flap Position Indicator & Lever |  | . . . . . . . .AGREE |
|  | BEFORE START |  |
| Int/Ext Preparation |  | COMPLETED |
| Oxygen |  | CHECKED/100% |
| Flight Instruments |  | SET |
| QNH/Aa |  | SET/CROSSCHECKED |
| Park Brake |  | SET |
| Fuel Control Switches |  | CUTOFF |
| Autobrake |  | RTO |
| Passenger Signs |  | AUTO |
|  | . . . . . . . . . . . . . . . . .Briefing . . . . . . . . . . . . . . . . . . |  |
| AIS & DDM Items |  |  |
| Runway State- Significant Weather |  |  |
| Emergencies - Performance Restriction |  |  |
| SID-Radio Aids Set-AFDS(LNAV,VNAV,Hdg,Alt) |  |  |
| Terrain Clearance - Transition Altitude |  |  |
|  | CLEARED FOR START |  |
| Hyd Demand Pump No. 4 |  | AUX |
| Hyd Demand Pump No. 1 |  | AUTO |
| Fuel Load & Pumps |  | CHECKED & SET |
| Packs |  | ONE ON |
| Beacon |  | ON |
| Doors (Prior to Pushback) |  | CLOSED |
|  | AFTER START |  |
| APU Selector |  | AS REQD |
| Anti-ice |  | AS REQD |
| Aft Cargo Heat |  | ON |
| Air Conditioning |  | SET |
| Recall / Status |  | CHECKED |
| FMC |  | UPDATED |
| T/O EPR |  | SET |
| Ref Speeds |  | SET |
| L. Nav / V. Nav |  | AS REQD |
|  | BEFORE TAKE OFF |  |
| Vital Data |  | RELEVANT |
| Flaps |  | ( ) GREEN |
| Flight Controls |  | CHECKED |
| Trim |  | UNITS & ZERO |
| Transponder |  | SET |
| Cabin Crew |  | REPORT RECD |
|  | . . . . . . . . . . . . . Entering Runway . . . . . . . . . . . . . |  |
| Exterior Lights |  | AS REQD |
| Cabin crew |  | SIGNAL |
|  | AFTER TAKEOFF |  |
| Landing Gear |  | UP & OFF |
| Flaps |  | UP |
| Air Conditioning |  | SET |
| Nacelle Anti-icing |  | AUTO |
|  | . . . . . . . . . . . Trans Altitude . . . . . . . . . . . . |  |
| Altimeters |  | STD/CROSSCHECKED |
|  | DESCENT BRIEFING |  |
| Safety Altitudes - Trans Level |  |  |
| U/S Items - Sig Weather - Handling Pilot |  |  |
| STAR - Approach |  |  |
| Runway State - Reverse - Brakes |  |  |
| Airfield |  |  |
| Go-Around - Diversion |  |  |
|  | DESCENT/APPROACH |  |
| Recall |  | CHECKED |
| Briefing |  | CONFIRMED |
| V ref |  | SET |
| Minima |  | SET |
|  | . . . . . . . . . . .Trans Level . . . . . . . . . . . . |  |
| Altimeters |  | QNH/CROSSCHECKED |
|  | LANDING |  |
| Speedbrake |  | ARMED |
| Autobrake |  | SET |
| Landing gear |  | DOWN |
| Flaps |  | ( ) GREEN |
| Cabin Crew |  | REPORT RECD & SIGNAL |
|  | AFTER LANDING |  |
| Strobes |  | OFF |
| Stabilizer |  | 6 UNITS |
| Speedbrake |  | DOWN |
| Flaps |  | UP |
| APU Electrics |  | AVAIL |
|  | . . . . . . . . . Approaching Stand . . . . . . . . . . |  |
| `Doors to Manual´ |  | CALLED |
|  | SHUTDOWN |  |
| Hyd Demand Pumps |  | OFF |
| Fuel Pump Switches |  | OFF |
| Aft Cargo Heat |  | OFF |
| Wx Radar |  | OFF |
| Park Brake |  | AS REQUIRED |
| Fuel Control Switches |  | CUT OFF |
|  | SECURE |  |
| IRS |  | OFF |
| Emergency Exit lights |  | OFF |
| Packs |  | OFF |
| APU |  | OFF |
| Ext Power |  | OFF |
| Standby Power Switch |  | OFF |
| Battery Switch |  | OFF |